## Slide 1: Connection/wiring diagrams for RC Car
The image at left shows the version using the IR Receiver.
We also have a version using Bluetooth instead.
Instructions for building the original car are here:
http://www.hitechnic.com/models
Note that we modified the car to hold an STM32 Discovery Kit
card that replaces the NXT Brick.
A video of their car is available on YouTube:
https://www.youtube.com/watch?v=KltnZBSvLu4

## Slide 2: The Battery
XTPower MP-10000 External Battery Pack with 10000mAh using dual USB 5V and DC 9V / 12V 2A
Ideal because it provides the 9V for the motors and sonar sensor, and 5V for the computer.
(Can use 12V for the motors if desired.)

## Slide 3: Modify the F4 Disco target board
You must disable the blue User button on the F4 Disco board so that the GPIO pin PA0 is available for use by the on-board app.
To do so, remove (de-solder) solder bridge SB20 described in UM1472 Discovery kit for STM32F407/417 lines document
  See Table 4 “Solder bridges”
  See Figure 16 for circuit

## Slide 4
NXT Shield
M1
M2
SONAR
Provides circuitry for the two motors and the sonar sensor
Kit, available for purchase from http://shop.tkjelectronics.dk/product_info.php?products_id=29

## Slide 5
5V
Gnd
M1
M2
Power to NXT Shield
red and black
wires
Gnd
9V
From battery
From battery

## Slide 6
M1, Tach1
M1, Tach2
M1, PWM
M1, P1
M1, P2
PA15
PB3
PB6
M1
M2
PA10
PB1
Motor1
NXT2:PA15, Tach1
NXT5:PB3, Tach2
NXT7:PA10, Polarity1
NXT9:PB6, PWM
NXT11:PB1, Polarity2
white
wires
Wire colors are not as used

## Slide 7
M2, Tach1
M2, Tach2
M2, PWM
M2, P1
M2, P2
PA0
PA1
PB4
M1
M2
PA2
PA3
Motor2
green
wires
NXT3:PA0, Tach1 (requires removal of solder bridge SB20)
NXT6:PA1, Tach2
NXT12:PA2, Polarity1
NXT10:PB4, PWM
NXT8:PA3, Polarity2
Wire colors are not as used

## Slide 8
Vin
5v
HiTechnic IR Receiver
Vin: 5V
Gnd: Gnd
Gnd
Gnd
SDA
PB9
PB8
SDA: PB9
SCL: PB8
Using I2C #1
SCL
Wire colors are not as used
Resistors are in the Altoids can.
Power and ground lines go to the Altoids can, then from there to the sensor.
The sensor lines go into the Altoids can.
Altoids container

## Slide 9
Vin
5v
Bluefruit LE Friend UART
Vin: 5V
Gnd: Gnd
Gnd
Gnd
MOD
PD0
CTS
PD3
RTS
PD4
MOD : PD0;
CTS : PD3;
RTS : PD4;
Tx : PD5; -- RXI pin on breakout board
Rx : PD6; -- TXO pin on breakout board
RXI
PD5
TXO
PD6
DFU is not connected
On USART #2
Wire colors are not as used

## Slide 10
Vin
5v
Bluefruit LE Friend SPI
Vin: 5V
Gnd: Gnd
Gnd
Gnd
SDA
PB11
SCL
PB10
RST
PB5
SDA: PB
SCL: PB
Wire colors are not as used

## Slide 11
PB11
PB13
M1
M2
Ultrasonic
Sensor
A4
A5
This is for a 9-volt sensor,
not an A/D sensor
SCL
SDA